## Slide 1: Robotic Perception and Action
ROS Homework

## Slide 2
Create a ROS package called homework in the current workspace.
All the directories, files and generated code must be inside the homework directory.
Rules

## Slide 3
Robot Modeling and Simulation
Create a new robot and simulate it in a virtual world in
gazebo. The robot structure must be different from the
robot explained during the lessons. The differences could
be in the robot sizes, number of wheels, number and type
of sensors ecc.
  Gazebo Plugin Requirements
  Differential Drive
  Sensor: Laser or Camera (Kinect, real sense...)
Index

## Slide 4
2) Data Acquisition
Create a subscriber node called acquire_data.cpp with the
aim to acquire data from the robot. The data to collect is
from the odometry (pose) and the sensor (laser scan or
point cloud data), during a motion of the robot. Show the
data acquired on the terminal during the motion of the robot
(manually with the teleop_twist keyboard) in the virtual
world simulated in gazebo.
The subscribers are:
Odometry
Sensor data
Index

## Slide 5
3) Sensor Fusion
Given the virtual world and the created robot,
create a node called fuse_data.cpp with the aim
to make the sensor fusion from the odometry
and the sensor data. The odometry must be corrupted
from a noisy signal. Show the results on the terminal.
The subscribers are:
Odometry
Sensor data
Homework

## Slide 6
ALTRE IDEE
Creare un nodo che pubblica comandi di velocità per far seguire al robot in maniera non manuale una traiettoria specifica
...
Homework